## Slide 1: FUSION Lidar processing and visualization software
Bob McGaughey
USDA Forest Service
Pacific Northwest Research Station
Vegetation Monitoring and Remote Sensing Team

## Slide 2: Overview
FUSION history & overview
Basic tools
Workflow tools
Future

## Slide 3: Initial LIDAR team (1998-1999)
Steve Reutebuch & Bob McGaughey
  USDA Forest Service, Pacific Northwest Research Station
  Steve retired in February 2016
Hans-Erik Andersen
  Then: University of Washington
  Now: USDA Forest Service, Pacific Northwest Research Station

## Slide 4: Our first LIDAR project (1998-1999)
Pre- and Post-treatment data acquired by helicopter
  ~800 ha
  SAAB TopEye scanner
  7000 pulses/second
  4-6 pulses/m2
  40 million points
  Delivered in ASCII text
Hypothesis was that you could NOT get adequate measurements of the ground surface under dense, Douglas-fir canopies typical in western Washington and Oregon
  We were wrong…

## Slide 5: Bare-earth accuracy
LIDAR DEM
Mean LIDAR DEM error compared to 350 survey points
  22 cm…9-inch field boot height!
Maximum errors:
  +1.31 meter, -0.63 meter
    +4.3 ft, -2.1 ft
Error was generally not affected by canopy density

## Slide 6: Our first LIDAR tools
Original dataset was 40 million points (all returns)
  We had to split the area into 4 tiles just to create a 1m gridded bare-earth surface
  Most software at the time (1999-2000) couldn’t handle the data
Our earliest software tools were designed for specific tasks (FORTRAN, C, C++, and IDL)
Visualization was essential to help us understand the data

## Slide 7: FUSION was born
We needed software tools to help us understand what was being measured by LIDAR…and what was not
As we learned more, the tools became more general and more flexible
In 2003-2004, we started working on a unified set of LIDAR tools that would support a variety of analysis tasks

## Slide 8: FUSION goes public
First public release in 2006
LAS support but most projects still delivered in ASCII text format
Support and training through the Forest Service’s Remote Sensing Applications Center (RSAC…now GTAC)
  Written and online tutorials
  Hands-on training

## Slide 9: Overall design
Focuses on applications in a forestry context
Programs (50+) are designed to accomplish specific tasks
Programs serve as building blocks for complex analyses
Point data are almost always subdivided so they can be loaded into memory—a few tools stream point data
Most point tools can clip rectangular areas and normalize using ground surfaces on-the-fly
Notes: Last 2 points are important: the size of the delivery tiles doesn’t really matter. We are starting to see more acquisitions with very large delivery tiles (1Gb +)

## Slide 10: Data exploration and visualization
LDV
Data
viewer
Color
Lighting
Glyph
Motion
Measurement
Sample options
  Shape & size
  Coloring rules
  Snap to POI
FUSION
Data
interface
Image
LIDAR data
Points of interest (POI)
Bare-earth model
Hotspots
Canopy model
Tree data
PDQ
Simple Data
viewer
Command line processing and utility programs
AreaProcessor
Notes: PDQ provides 3D viewing and manipulation for LAS, FUSION, ASCII LIDAR data and FUSION surface models

## Slide 11: Demo FUSION & LDV

## Slide 13: Measuring tree attributes
Notes: Hidden for presentations that include a live demo of FUSION and LDV software

## Slide 14: Individual tree heights
Study carried out in Fort Lewis Military Reservation, WA
Accurate tree height measurements obtained using surveying instruments (total station) & least squares adjustment
Average error of tree top measurements from survey: 2 cm!
Lidar tree hts. measured in FUSION software

## Slide 15: Individual tree heights
Tree heights from narrow beam LIDAR (-0.73 ± 0.43 m) more accurate than wide beam (-1.12 ± 0.56 m)
LIDAR heights for Ponderosa pine (-0.43 ± 0.13 m) more accurate than for Douglas-fir (-1.05 ± 0.41 m)
Heights from conventional field techniques (-0.27 ± 0.27 m) are more accurate than heights from LIDAR (-0.73 ± 0.43 m)
Notes: Source: Andersen et al., Can. J. of Remote Sensing, In review.

## Slide 16: Pulse density and tree heights

## Slide 17: Command-line toolkit
Point Cloud tools
  Clipping (circle, rectangle, and polygon) & merging
  Thinning
  Filtering (ground and outlier)
  Compute metrics
Surface tools
  Grid and TIN creation
  Clipping & merging
  Compute metrics (CHM and topo)
Conversion tools
  To/from various formats
  Mostly from FUSION-specific formats to ASCII raster then rely on GDAL for other formats
Miscellaneous
  Intensity images
  Tree segmentation (watershed & local maxima)
  QA tools

## Slide 18: Forestry applications
Direct use of surface and point data
  Hydrology, topographic metrics, microclimate conditions
  Vegetation height (CHM – ground)
  Presence/absence of trees (large trees)
  Canopy cover (proportion of 1st returns above height threshold)
Derived products
  Area-based approaches for inventory
  Clump/gap analyses
  Forest structure
  Individual tree

## Slide 19: Canopy cover
# first returns in canopy (13)
Total # first returns (20)
65%
=

## Slide 20: Area-based approach (ABA) for modeling
Relies on field measurements and lidar collected during the same growing season (ideally)
Relate lidar-derived metrics to summarized field attributes by developing statistical models
Apply model to lidar-derived metrics covering entire acquisition to map attributes over large areas

## Slide 21: ABA steps
Given a set of field plots with accurate locations:
  Clip point data corresponding to the plot area
  Normalize point elevations using ground surface
  Compute metrics using normalized points
  Fit model(s) to related lidar-derived metrics to field attributes
  Compute metrics over entire acquisition area using cell size that matches the plot size
  Apply the model(s) to map attributes

## Slide 22: ABA steps
Given a set of field plots with accurate locations:
  Clip point data corresponding to the plot area
  Normalize point elevations using ground surface
  Compute metrics using normalized points
  Fit model(s) to related lidar-derived metrics to field attributes
  Compute metrics over entire acquisition area using cell size that matches the plot size
  Apply the model(s) to map attributes

## Slide 23: Metrics used for structure classes
Dominant tree height -
95th percentile*
Dominant lower foliage height -
25th percentile*
Cover 2-8 m
*Returns ≥2 m
Cover 8-16 m
Cover 16-32 m
Cover >32 m
Canopy profile**
Structural complexity –
rumple (rugosity)

## Slide 24: Structure classes
Class 1
Short
Open
p95*=20m cvr >2m=16%
Class 2
Shorter
Multi-story
Sparse
p95*=20m cvr >2m=34%
Class 3
Shorter
Multi-story
Sparse
p95*=20m cvr>2=44%
Class 4
Shorter
Multi-story
Clump-gap
p95*=22m cvr>2=62%
*median class values

## Slide 25: Structure classes
Class 9
Tallest
Topstory
Clump-gap
p95*=45m cvr>2=71%
Class 8
Taller
Topstory
Clump-gap
p95*= 34m cvr>2=69%
Class 7
Taller
Topstory
Clump-opening
p95*=32m cvr>2=49%
Class 6
Mid-height Mult-story
Clump-gap
p95*=29m cvr>2=69%
Class 5
Mid-height Mult-story
Clump-opening
p95*=26m cvr>2=51%
*median class values

## Slide 26: Individual trees
Detect trees using CHM
Add point cloud metrics for each tree
Use as individual trees
Aggregate over areas and summarize

## Slide 27: Workflow tools
Workflow generator—AreaProcessor (AP)
Terminology
  Delivery tiles: Point tiles (LAS or LAZ) delivered by the data provider
  Processing tile: Set of points submitted to all of the tools. Typically these are clipped from the delivery tiles and include a “buffer” around the tile.
  Processing block: Collection of processing tiles that will be processed by a single processing thread. Processing blocks also provide a structure for outputs.

## Slide 28: AP workflow
Workflows can support a variety of processing tasks
  Standard scripts included with the distribution produce a variety of outputs
  Outputs can be turned ON or OFF
  Savvy users can use the workflow in non-standard ways or with non-FUSION tools
Single or multiple processing threads
Always a single-entry point to start the processing
Separate monitoring tool provides visual display of progress

## Slide 29: AP workflow
Clip
Process
Check for errors
Configuration
GUI interface
Batch file
Extract & merge
User-defined processing steps
Processing runs on several cores/threads
For each processing tile:
Notes: In the scripts provided with the AP distribution, the setup batch file turns various products on/off and sets options to control merging of products, cell sizes, and ground surface options. The configuration parameters specified in the GUI are more general and serve to identify the overall run.

## Slide 30: Progress monitoring
Colors represent cores/threads
Smallest areas are processing tiles
Larger areas (colored) are processing blocks

## Slide 31: Progress monitoring
Green is good
Yellow is in-process
Red indicates errors

## Slide 32: Products
Standard set of outputs produced using scripts distributed with FUSION
Raster data in ERDAS IMAGINE format (200+ layers)
  First-return metrics (elevation and intensity)
  All-return metrics (elevation and intensity)
  Metrics by height strata (all and first returns in 11 strata)
  Canopy height models
  Canopy height surface metrics
  Intensity images
  Bare-ground surface models (optional)
  Topographic metrics
Shapefiles for delivery tiles, ground models, processing tiles & processing blocks

## Slide 33: Where is FUSION used?
Users across the U.S and several other countries.
  I usually only hear about new users when something goes wrong or someone wants to do something “unusual” with their data
Training
  RSAC has trained over 2000 people through 1-3 day training sessions
  Workshops covering FUSION presented in Mexico, Brazil, & Philippines
Web tracking active from 2013-2016 showed 400-600 downloads/month
Forest Service western regions have active lidar programs and use FUSION for quality assessments and to produce product sets
  I know less about eastern regions but know there is lidar activity and FUSION use
University teaching and research (international)

## Slide 34: Future?
Past…
  FUSION & data viewers are built on Windows GUI
  Command line tools rely on Microsoft Foundation Classes
  Source code has always been available but not “advertised”
  Releases prior to 2020 were built using MS VC6
Future…
  Ideally code will move onto github
  Tested with 2 programs (with help from Howard Butler)
    Build actions work for windows platform
  Movement to any other platform is unlikely

## Slide 35
Download link
  http://forsys.sefs.uw.edu/fusion/fusionlatest.html
Tutorials
  Search (google) for “RSAC lidar”
  https://www.fs.fed.us/eng/rsac/lidar_training/
Manual (included in download)
  http://forsys.sefs.uw.edu/software/fusion/FUSION_manual.pdf